Tender Specifications AVK Surface Box CPH HD-GG [80/21-200]

1. Range

Surface Box CPH / fixed height 293 mm / HDPE

2. Product description

General

The surface box shall be for installation in roads, sidewalks or green zones to provide access to underground valves in water or gas lines.

Basic design

The surface box design shall correspond with AVK Surface Box CPH HD-GG series 80 type 21 variant 200 (STV 80/21-200) or equivalent.

Product shall be a heat resistant, synthetic surface box with a cast iron GJL-200 lid attached to the housing by a galvanized steel cable.

Housing shall consist of one part made out of HDPE material.

Features

Surface box shall have a max. total weight of 3 Kg.

Housing shall be 100% corrosion-free.

Housing and lid shall be designed to ensure easy opening at all times

Surface box housing and lid shall have a heat resistance of at least 160 °C.

Surface box shall meet B125 load bearing capacity, tested by applying flat load on top surface.

Surface box housing shall have an extra wide bottom flange (at least twice the width of top diameter) for enhanced support.

Lid shall provide space for two inscription plates.

3. Sustainability

Surface box shall have a carbon footprint of max. 5 Kg. Carbon footprint (CO2 emission) shall be calculated by using Lifecycle Assessment method according to ISO 14040-44. 
Housing to be made of 100% first grind recycled thermoplastic material.

Housing and lid to be 100% recyclable after end of life.

Surface box shall contain no heavy metals or any other contamination.